## Slide 1: NAT & PAT
Course Code: CSC 3116
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | Lab 11 | Week No: | 11 | Semester: | Summer 22-23
Lecturer: | Shakila Rahman; Shakila.Rahman@aiub.edu |  |  |  | 
Course Title: Computer Networks

## Slide 2: Lecture Outline
Static NAT
Dynamic NAT
PAT

## Slide 3: Static NAT
Configuration
Configure the routers and PCs as usual
Perform routing
NAT(config)#int fa0/0
NAT(config-if)#ip nat inside
NAT(config)#int fa0/1
NAT(config-if)#ip nat outside
NAT(config)#ip nat inside source
static 192.168.1.1 195.15.2.3
To be replaced
Replaced by
Net: 192.168.1.0/24
Net: 192.16.2.0/24
Net: 195.5.2.0/24
192.168.1.1
0009.7C45.2C4E
192.168.1.254
0002.1639.B801
195.5.2.1
0002.1639.B802
195.5.2.2
0030.F22D.9502
192.16.2.1

## Slide 4: Static NAT
Frames and Packets
Incoming PDUs at NAT
Net: 192.168.1.0/24
Net: 192.16.2.0/24
Net: 195.5.2.0/24
192.168.1.1
0009.7C45.2C4E
192.168.1.254
0002.1639.B801
195.5.2.1
0002.1639.B802
195.5.2.2
0030.F22D.9502
192.16.2.1

## Slide 5: Static NAT
Frames and Packets
Outgoing PDUs at NAT
Net: 192.168.1.0/24
Net: 192.16.2.0/24
Net: 195.5.2.0/24
192.168.1.1
0009.7C45.2C4E
192.168.1.254
0002.1639.B801
195.5.2.1
0002.1639.B802
195.5.2.2
0030.F22D.9502
192.16.2.1

## Slide 6: Dynamic NAT
Configuration
NAT(config)#int fa0/0
NAT(config-if)#ip nat inside
NAT(config-if)#int fa0/1
NAT(config-if)#ip nat outside
NAT(config)#ip nat pool mypool 195.15.2.3 195.15.2.100
netmask 255.255.255.0
First IP
Last IP
NAT(config)#ip nat inside source list 1 pool mypool
NAT(config)#access-list 1 permit 192.168.1.0 0.0.0.255
IP in the range 192.168.1.0 to 192.168.1.255 will only be translated

## Slide 7: Dynamic NAT….
Sample network for dynamic NAT illustration
Fa0/0
Fa0/1
Fa0/0
Fa0/1
192.168.1.1
192.168.1.2
192.16.2.1

## Slide 8: Dynamic NAT….
Sample network for dynamic NAT illustration
(a) Incoming IP header at fa0/0 from PCX
(b) Outgoing IP header at fa0/1 from PCX
(c) Incoming IP header at fa0/0 from PCY
(d) Outgoing IP header at fa0/1 from PCY

## Slide 9: PAT
NAT(config)#int fa0/0
NAT(config-if)#ip nat inside
NAT(config-if)#int fa0/1
NAT(config-if)#ip nat outside
NAT(config)#access-list 1 permit 192.168.1.0 0.0.0.255
IP in the range 192.168.1.0 to 192.168.1.255 will only be translated
NAT(config)#ip nat inside source list 1 interface
fastethernet 0/1 overload

## Slide 10: PAT….
Verifying Configurations of NAT and PAT

## Slide 11
References
[1] S. Empson, CCNA Portable Command Guide, 2nd ed., Cisco Systems, Inc., 2008, USA.

## Slide 12
Recommended Books
  Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.